## Slide 1: 디지털 시스템 실습
실험8. 부프로그램

## Slide 2: 부프로그램
VHDL 구문에서는 고급언어와 마찬가지로 부프로그램(subprogram)을 정의할 수 있다.
이 부프로그램은 C언어와 같이 function(함수)과 procedure(프로시져)로 나눌 수 있다.
function과 procedure는 자주 쓰이는 설계의 일부분을 따로 작성하거나, 기능적으로 분해 가능한 프로그램의 일부를 분리해서 작성할 수 있다.
procedure와 function의 [구성]은 순차처리문으로 되어 있다.
하지만 procedure와 function의 [호출]은 순차처리문, 병행처리문 함께 사용 할 수가 있다.
부프로그램을 작성하는 위치는 architecture선언부(architecture와 begin 사이), process문의 선언부(process와 begin 사이)에서 작성하거나 혹은, package에서 작성한다.
procedure와 function은 일반적으로 입출력 매개변수에 vector의 길이를 지정하지 않는다.
이것은 그 부프로그램이 vector의 길이가 매개변수로 전달되고 호출된다는 것을 뜻한다.

## Slide 3: 예제: procedure 선언과 호출
procedure calc( signal a, b : in std_logic_vector;
signal c, d : out std_logic_vector ) is
begin
c <= a + b;
d <= a - b;
end calc;
architecture sample of pro1 is
begin
calc( x, y, add_out, sub_out ); -- 병행호출
end sample;
process(x, y)
begin
calc( x, y, add_out, sub_out ); -- 순차호출
end process;

## Slide 4: 예제: 부프로그램 - architecture 선언
library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all;
entity calcp1 is
port ( x, y : in std_logic_vector(3 downto 0);
add_out, sub_out : out std_logic_vector(4 downto 0) );
end calcp1;
architecture sample of calcp1 is
procedure calc( a, b : in std_logic_vector;
c, d : out std_logic_vector ) is
begin
c := a + b;
d := a - b;
end calc;
begin
process(x, y)
variable temp1, temp2 : std_logic_vector( 4 downto 0 );
begin
calc( x, y, temp1, temp2 );
add_out <= temp1;
sub_out <= temp2;
end process;
end sample;

## Slide 5: 예제: 부프로그램 - process 선언
library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all;
entity calcp2 is
port ( x, y : in std_logic_vector(3 downto 0);
add_out, sub_out : out std_logic_vector(4 downto 0) );
end calcp2;
architecture sample of calcp2 is
begin
process(x, y)
procedure calc( a, b : in std_logic_vector;
c, d : out std_logic_vector ) is
begin
c := a + b;
d := a - b;
end calc;
variable temp1, temp2 : std_logic_vector(4 downto 0);
begin
calc(x, y, temp1, temp2);
add_out <= temp1;
sub_out <= temp2;
end process;
end sample;

## Slide 6: 예제: 부프로그램 - package 선언
library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all;
package mypack1 is
procedure calc( a, b : in std_logic_vector;
c, d : out std_logic_vector );
end mypack1;
package body mypack1 is
procedure calc( a, b : in std_logic_vector;
c, d : out std_logic_vector ) is
begin
c := a + b;
d := a - b;
end calc;
end;

## Slide 7: 실습1
기본이론에서 작성한 package mypack1내의 procedure calc을 호출하는 VHDL 프로그램을 작성해 보자.

## Slide 8: 실습1
library ieee;
use ieee.std_logic_1164.all;
use work.mypack1.all;
entity calcp5 is
port ( x, y : in std_logic_vector(3 downto 0);
add_out, sub_out : out std_logic_vector(4 downto 0) );
end calcp5;
architecture sample of calcp5 is
begin
process(x, y)
variable temp1, temp2 : std_logic_vector(4 downto 0);
begin
calc( x, y, temp1, temp2 );
add_out <= temp1;
sub_out <= temp2;
end process;
end sample;

## Slide 9: 과제 1
다음의 procedure을 architecture선언부, process문의 선언부 및 package에서 작성하라.
procedure maxmin( a, b : in std_logic_vector(4 downto 0);
c, d : out std_logic_vector(4 downto 0));
출력 'c'는 a와 b의 값 중 작은 수가 출력되고, 출력 ‘d’는 a와 b의 값 중 큰 수가 출력된다.

## Slide 10: 부프로그램: function-return
function은 함수선언과 함수몸체로 정의, 지연(delay) 없이 계산의 결과를 return하는 부프로그램이 사용된다.
따라서 그 내부에는 wait문을 포함할 수가 없다.
function과 procedure의 차이점은 다음과 같다.
  function은 되돌려주는 값(return value)이 단 하나지만 procedure의 경우는 여러 개가 될 수 있다.
  function의 매개변수(parameter)의 mode는 지정하지 않더라도, in mode이지만 procedure의 매개변수의 mode는 in, out, inout가 될 수 있다.
  function은 지연 없는 계산에 쓰이는 수식의 중간에 사용되나 procedure는 수 식의 중간에 사용할 수 없다.
  function은 wait문을 사용할 수 없으나 procedure는 wait문을 사용할 수 있다.
  function과 procedure에 사용되는 VHDL문장은 모두 순차처리문이어야 한다.
  function과 procedure를 호출하는 방식은 순차호출과 병행호출이 있다.

## Slide 11: 예제: 부프로그램 - architecture 선언
library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all;
entity maxf is
port( a, b : in std_logic_vector(7 downto 0);
y_out : out std_logic_vector(7 downto 0) );
end maxf;
architecture sample of maxf is
function max(x, y : in std_logic_vector) return std_logic_vector is
variable temp : std_logic_vector(7 downto 0);
begin
if x > y then
temp := x;
else
temp := y;
end if;
return(temp);
end max;
begin
process(a, b)
begin
y_out <= max(a, b);
end process;
end sample;

## Slide 12: 예제: 부프로그램 - process 선언
library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all;
entity maxf2 is
port( a, b : in std_logic_vector (7 downto 0);
y_out : out std_logic_vector (7 downto 0) );
end maxf2;
architecture sample of maxf2 is
begin
process(a, b)
function max(x, y : in std_logic_vector) return std_logic_vector is
variable temp : std_logic_vector(7 downto 0);
begin
if x > y then
temp := x;
else
temp := y;
end if;
return(temp);
end max;
begin
y_out <= max(a, b);
end process;
end sample;

## Slide 13: 예제: 부프로그램 - package 선언
library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all;
package mypack2 is
function max(x, y : in std_logic_vector) return std_logic_vector;
end mypack2;
package body mypack2 is
function max(x, y : in std_logic_vector) return std_logic_vector is
variable temp : std_logic_vector(7 downto 0);
begin
if x > y then
temp := x;
else
temp := y;
end if;
return(temp);
end max;
end mypack2;

## Slide 14: 실습2
기본이론에서 작성한 패키지 mypack2내의 함수 max(x,y)를 병행호출과 순차호출 방식으로 작성.

## Slide 15: 실습2
library ieee;
use ieee.std_logic_1164.all;
use work.mypack2.all;
entity maxf4 is
port( a, b : in std_logic_vector (7 downto 0);
y_out : out std_logic_vector (7 downto 0) );
end maxf4;
architecture sample of maxf4 is
begin
process(a, b)
begin
y_out <= max(a, b);
end process;
end sample;
library ieee;
use ieee.std_logic_1164.all;
use work.mypack2.all;
entity maxf5 is
port( a, b : in std_logic_vector (7 downto 0);
y_out : out std_logic_vector (7 downto 0) );
end maxf5;
architecture sample of maxf5 is
begin
y_out <= max(a, b);
end sample;
순차호출
병행호출

## Slide 16: 과제2
위의 예에서 max(x, y)을 순차호출과 병행호출방식으로 함수를 작성하였다.
이것을 min(x, y)에 대해서도 같은 방식으로 설계하라.
단 min(x, y)는 두수 x, y 중 작은 값을 return 값으로 정한다.